Internet Measurements: the Rising Tide and the DNS Snag

Christian Huitema & Sam Weerahandi

Telcordia Technologies, Morristown, NJ

huitema@huitema.net, swrs@research.telcordia.com

January 28, 2000

# Abstract:

In September 1998, we started to measure the quality of web service by selecting and polling a random set of 100 web servers every day. Starting April 1999, we also began a control experiment by polling a fixed set of large servers every day. We obtained measurements of the main phases of the connection, the name resolution, the TCP connection, the resolution of the HTTP GET, the duration of the transfer and the size of the page. We analyzed the measurements collected until January 2000. We observed that the median data rate of the TCP connection increased from 40 kbps to 70 kbps during that period, while the median round trip delay decreased from 200 to 130 milliseconds. We can determine, from the analysis of the delays, the percentage of connection attempts that needed to be repeated and the distribution of the queuing delays. The percentage of repeated requests dropped from 10% to about 4% during the experiment. The distribution of queuing delays measured during our sampling appear to follow a power law.

The experiment helped us evidence a  problem in the current web service, the quality of the domain name service. Name resolution, through the standard "gethostbyname()" interface, took longer than 2 seconds in 29% of our trials. We are not a special, aberrant case: control sites reported that in 24% to 32% of their trials, name resolution also took longer than 2 seconds. The main culprit is the flat structure of the domain name space, especially in the most popular domains, .com, .net and .org. This flat structure reduces the effectiveness of caching, and also concentrates the burden of solving names for the whole Internet on a very small set of servers. It is quite obvious that some of these servers cannot handle the load.

# Introduction

In September 1998, we started a simple measurement experiment. We wanted to get an idea of the overall performance of the Internet at large. In this experiment we are not concerned with the performance of individual network elements, something we also do as part of another experiment which we do not report here due to the proprietary nature of underlying methodologies. Instead, we look at the overall performance of the Internet over time as experienced by an end user of the web, a user from Telcordia in our case. Of course, there are many contributors to performance improvement or deterioration over time, ranging from changing backbone capacity to congestion at servers, but the question is what do they all mean to an end user. Moreover, we base our conclusions on findings from a random sample of web servers and analysis of aggregate results over time, thus minimizing the variation of observed quality metric in individual measurements due to jitter, outbound and inbound paths, etc.

In particular the results from this type of study can help resolve the validity of various assertions and hypotheses. For example, we read assertions that the quality of the Internet was degrading over time, or remained stable. On the other hand, the major Internet Service Providers were increasing the capacity of their backbones, installing more and more OC48, OC96 and even OC192 trunks, using WDM. There seemed to be a contradiction. Would we see the Internet service driven to the ground, or would we on the contrary observe a rising tide, where the increased capacity would lift the quality experienced by many applications?

We wanted to design an experiment that would be easy to replicate, easy to conduct, and that would as much as possible provide an idea about the quality level of the global Internet. Many experiments used special purpose measurement servers [1, 2], but we decided to simply perform connections to a sampling of web sites. The web sites are chosen from a list of sites, constructed by a simple "web spider." When we begun the experiment, our spider had collected a list of about 100,000 names. We add more site names everyday, so that by January 2000 the database contains more than 500,000 names.

We also wanted to conduct our test during a busy hour of the Internet, so that time of the day effects will not add with our study of day to day performance change over time. So we chose to start the test everyday at 3 pm EST, an hour when businesses are active throughout North America. Everyday, we picked 100 servers at random from our database, and tried to load the home page of each of these servers. Some connection attempts would fail, either because the name in our database was invalid, or because the server was unreachable. In that case, we would pick new servers names at random in the database, until we completed a total of 100 connections per day. For each connection attempt, we measured several variables, such as:

- the DNS delay, i.e., the duration of the "gethostbyname" command,

- the connection delay, i.e., the duration of the "connect" command,

- the delay that elapses between the sending of the HTTP "GET" command and the reception of the first byte of data from the web server,

- the delay necessary to complete the reception of the page,

- the length of the page measured in bits.

Although these measurements are taken from individual sites, our analysis, with the purpose of demonstrating trends as explained above, applies only to the aggregation of all sites in the samples.

Picking server names at random introduces a bias. It privileges the small sites that users find through search engines, rather than large web portals that attract a large share of the traffic. Starting in April 1999, we conducted a control experiment, by also connecting to a fixed set of 100 large servers every day. The experiment provided us interesting data on the evolution of the available bit rates, observed delays and loss rates. It also documented a major problem with the current domain name service.

# What is the prevalent bandwidth?

In this context, by bandwidth we mean the throughput, the bits per second obtained by the user, an end-to-end service quality metric, rather than the physical bandwidth of an individual link in the Internet. It is also close to the bandwidth of a bottleneck on the path between the user and the web server, at a given instant. When it comes to web service, one key measure of quality is the time needed to load a page. An important factor in that time is the bandwidth of end-to-end connection. We estimate the bandwidth per connection by a simple division of the length of the page in bits by the duration of the connection in seconds. The values that we observed during the experiment are summarized in the following figure, in which each day's measurement is summarized by the median value amongst our 100 tests and by the maximum bandwidth achieved by the 5% connections with lowest bandwidth, which we call below as worst 5% for simplicity.

The experiment, so far, has only lasted 15 months, but it seems to indicate that the bandwidth is, in general, increasing over time. Indeed, this result is only indicative of the performance observed at our site, an industrial research center connected to a major provider through several T1 connections. In fact, one may observe a sudden increase in the observed value in the summer of 1999. This was caused by a change of our local configuration, including a higher bandwidth and a cache server. This change led us to discard the data collected between the last weeks of July and the end of August in the further analysis.

An interesting observation is that the median value of observed bandwidth, which is close to the bottleneck bandwidth, at the beginning and end of the experiment is in line with the prevalent modem speed at these times, i.e., 40 kbps versus 28.8 kbps in September 1998, 70 kbps versus 56 kbps in January 2000. To understand this, we observed another parameter, the server's share of the delay, which we define as the ratio of the delay between the GET command and the arrival of the first bytes of data to the total duration of the connection. During our whole experiment, this ratio remained in the same band, varying between 30% and slightly more than 40%. This suggests that, at least statistically, the behavior of the web site managers is rationale. They would monitor the performance of their service, and invest in more capable servers or larger bandwidth if the performances fell under some threshold. We cannot guess what threshold they use, but a reasonable hypothesis is that a server is considered adequate when it can saturate the prevalent connection, which today is a modem connection.

Indeed, not all servers have good performance all the time. On the evolution graph, we can see that the 5% worst case remained of the order of a few kilobits. But then, some servers are also quite fast. On the above figure, we plot the cumulative frequency distribution of the observed bandwidth, for the duration of the experiment. We observe that while the median value for the whole period is about 30 kbps, 30% of the connections had a speed above 100 kbps, and that in a fair number of cases, we could observe speeds of several 100 kbps, sometimes higher than 1 Mbps. This means that an internaut who invests today in a faster Internet connection, such as DSL or Cable Modem, will indeed get better performances, at least for a fraction of the time. It also means, if our hypothesis on the behavior of site managers is true, that the tide will go on rising, as more and more sites increase their threshold of quality from "modem compatible" to "broadband ready."

# Distribution of connection delays and packet loss rates

One way of characterizing the quality of service is by the three parameters, bandwidth, transmission delay and packet loss rate. We estimate the prevalent transmission delays and packet loss rates by analyzing the distribution of the TCP connection delays, which we obtained by clocking the connect() commands. Over the duration of the experiment, the delays evolved nicely, as shown on the following graph.

As mentioned in the previous section, the low values in August 1999 are an artifact of our configuration, due to the insertion of a cache server in the network. If we disregard these values, we observe that the median delay (shown in the connection delay chart is also the moving average, abbreviated as Mov. Avg. here and in future references, medians of window size 14) of our connections to random sites decreased from about 200 milliseconds in September 1998 to about 130 millisecond in January 2000. This is indeed another sign of a rising tide of quality. The natural explanation is that, as we move to higher speeds in the backbone and in the connection to most corporate networks, the packet transmission delays are slowly converging towards the natural limit that the speed of light in optical fibers dictates.

We observe that the distribution of the connection delays has an irregular structure. Most connection delays (denoted below as C) are relatively short, but that a significant fraction of the delays are quite long, larger than 2 seconds. This is easily understandable when we look at the implementation of the "connect()" command. The connecting node sends a TCP SYN packet to the selected server, and waits for a SYN ACK. If the response fails to come back after a delay of about 3 seconds, the connecting node repeats the initial packets. It is indeed theoretically possible that the repetition be caused by extremely long transmission delays of the SYN or SYN ACK packets, but our data suggest that the bulk of the long delays is caused by losses and repetitions.

This observation means that we can deduce the prevalent packet loss rate by observing the fraction of the connection attempts that lasted more than some long delay, for example two seconds. (We will discuss the choice of that specific value in the following paragraphs.) Again, the results are quite encouraging. As the quality tide rises, the fraction of attempts that had to be retried went from about 10% to less than 5%.

However, we should not jump too soon to the optimistic conclusion that the lower delays and the reduced loss rate will automatically enable new real-time applications, such as for high example high quality Internet telephony.  For one, a transaction loss rate of less than 5% means that the packet loss rate is still above 2%, a value that remains too high for most audio codecs. Even if we could somehow deal with this loss rate through a combination of loss concealment and forward error correction, we must also observe that even if the delays tend to become lower, they remain very variable.

To understand how variable these delays can be, we considered the subset of the connections that could be established in less than 2.5 seconds, and we plotted on a log scale both the density of the distribution and the cumulative frequency distribution, or rather the complement to 1 of the CFD. The results are quite interesting. The chart shows that the short delays are distributed between a few tens of milliseconds and slightly more than a hundred milliseconds, which may reflect the distribution of network distances between the servers and our site. More interestingly, the chart also shows that the tail of both the density and the CFD complement are approximately straight lines between 150 ms and 1.5 s. This suggests that tail of the distribution of delays and of the CFD can be described by a power law, of the form:

p(t) = at.

p(t>T) = at/(-1).

The best fit correspond to a value of  between -2.6 and -2.7. This kind of heavy tail distribution is consistent with other observations on the self similar nature of Internet ( or Ethernet) traffic [3,4]. This kind of distribution suggests that, despite the increase in the capacity of access links and backbone trunks, a significant fraction of the transmission delays is spent in queues, that have to absorb the high variability of the Internet traffic.

In the chart, the density of the high values, above 1.5 second, is not described by as straight a line as the values between 0.1 and 1.5 second. We only plotted 38,302 connection attempts, which means that we cannot precisely estimate the values of regions where the density is less than 1/10000.  We can however use the values that we just computed to build a model of the density and CFD functions. Using that model, we predict that, in the absence of losses, about 0.6% of the connection delays would exceed 2 seconds, and about 0.3% would exceed 3 seconds. When we decided to observe the fraction of connection delays that exceeded 2 seconds in order to estimate the probability of packet losses, we introduced an error, the risk, in the current Internet, to overestimate the occurrence of repetitions by 0.6%. Instead of the value of 10% in September 1998 and 5% in January 2000 that we mentioned above, we may possibly only have repeat rates of 9.4% or 4.4%. However, this does not change the general trend.

# Analysis of the DNS delays

Our tests use randomly picked server names. This implies that, in most cases, the local name servers never heard of the name before we start our test. The address of the tested server will not be present in the local cache, and will have to be retrieved through a succession of requests.  In a typical case, in order to resolve "www.example.com", we will see the following:

- Our client uses "gethostbyname()" to ask the address of "www.example.com". The local resolver sends a request to the local DNS server.

- The local server, which does not have a copy of the information in its cache, relays the request to a top level domain server, one of the servers for ".com" in our example.

- The top level domain server sends back the address of the name server for the selected domain, such as "ns.example.com."

- The local server sends the initial request for "www.example.com" to the domain name server, "ns.example.com."

- The domain name server sends back the address of the web server.

- The local server provides the information to the local resolver.

At each stage, timers can trigger repetition of messages, to protect against losses. The name resolution delays will thus include network transmission delays, queuing delays, and in some cases timer delays. The plot of the cumulative frequency distribution of the DNS resolution delays shows two marked inflexion points, at respectively 2 seconds and 3 seconds.  These two points most likely correspond to two values of the DNS retransmission timers, in different DNS servers.  According to the chart, almost 30% of the DNS queries suffer from at least one retransmission. This is a surprisingly high number, in fact one of the major surprises in our measurements. Moreover, a plot of the fraction of delays, denoted by D, that are larger than 2 seconds shows that the situation is getting worse, even as the repetition rate of connection attempts is getting better.

The analysis of connection delays, denoted by C, showed that on average, between September 1998 and January 2000, about 6% of the connection attempts had to be repeated. The decomposition of our example only showed three transactions, one of which was local. If we assumed that local transactions are reasonably safe, and that repetitions would only be caused by packet losses in the network, we would expect that about 12% of the DNS name resolution would incur at least one repetition. Obviously, there is something else going on, something that we have to explain.

# Explaining the DNS delays

A likely explanation of the DNS resolution delays would be that some name servers are overloaded, and that the losses of packet occur either in the access lines leading to these servers, or in overflowing queues inside the servers. The question, then, is to find out which servers are overloaded and which are not. To do that, we analyzed the data from our database of nearly 500K web servers and classified the queries according to several criteria.

The first hypothesis was that the probability of experience repetitions depended of the structure of the name being resolved. Many names have three components, as "www.example.com," but others have just two, as "example.com," and yet others have four components, as "www.research.example.com", or even more. More name components imply more transactions over the network, which could imply more risk of losses. In order to assess whether the structure of names was a significant factor, we classified the names used in the sampling according to their number of name parts, and we computed the number of requests that took longer than 2 seconds for each category:

| Name parts in name | Fraction of requests with repetition |
| --- | --- |
| 2 | 32.98% |
| 3 | 30.51% |
| 4 | 18.34% |
| 5 | 15.44% |
| 6 | 19.86% |
| 7 or more | 52.38% |

We expected resolution of complex names to take longer, to be more prone to repetitions, and we observed the opposite. Whether the name contained 3 parts or only two did not seem to make much difference, but names that contained 4 parts were resolved faster, with less than 20% of resolutions affected by repetition, instead of more than 30% for shorter names. Names that contained five parts were resolved even faster. In fact, only the pathological cases of name containing more than 7 parts showed worse performances than the simple names. Possible explanations of this counter intuitive result may be that the most significant parts of structured names have more chances to be cached. Another possible explanation is that long names are possibly used by large organizations, who can afford high performance name servers.

We tried then to classify the names in our database according to the of the top level domains, computed again the fraction of requests that had to be repeated for each category, and found a that performance varied widely among domains. At this point, one could quickly jump to a conclusion that the main factor in the DNS performance is the quality of the name servers for the top level domain. However, other factors have to be at play there, since for example ".net", ".com" and ".org" share the same servers, yet exhibit different performances.

| Domain | % > 2 sec | % > 3 sec | Nb tests |
| --- | --- | --- | --- |
| .jp | 9.21% | 7.49% | 467 |
| .edu | 10.57% | 6.75% | 3140 |
| .gov | 13.62% | 9.86% | 426 |
| .au | 16.35% | 10.99% | 746 |
| .de | 21.78% | 14.67% | 900 |
| .us | 22.63% | 11.57% | 579 |
| .ca | 22.85% | 16.51% | 757 |
| .uk | 23.38% | 14.40% | 1514 |
| .net | 24.90% | 16.73% | 1960 |
| .com | 31.82% | 21.39% | 22716 |
| .org | 46.23% | 31.49% | 2931 |

To assess the role of the name servers, we designed a small experiment. We selected random server names, submitted them for resolution directly to selected root servers, waited for the results to come back, and measured the loss rate, i.e.,the fraction of request for which we received no response in 30 seconds. We performed the tests in January 2000, at the same busy hour during which we performed our other tests. We applied the test to the 5 most popular domains in our data set.  When several name servers were listed for a domain, we tested all of them, and computed the average loss rate over all servers. The results are listed in the following table, in which the last column is the repetition rate observed in the main experiment:

| Domain | Loss rate | Rep rate of Main experiment |
| --- | --- | --- |
| .com | 22.6% | 31.82% |
| .edu | 18.6% | 10.57% |
| .net | 11.9% | 24.90% |
| .org | 13.7% | 46.23% |
| .co.uk | 10.6% | 23.38% |

The results are somewhat surprising, since they show different loss rates for the ".com", ".org" and ".net" domains. We can only suppose that different resources are allocated to different domains inside these servers. We also observe that the results are only loosely related to the values that we observed in the main experiment. This may be due to the averaging of packet losses over all the servers of the domain. The servers have indeed widely different performances, as shown in the following table:

| Server | Loss rate |
| --- | --- |
| A.ROOT-SERVERS.NET | 33.9% |
| B.ROOT-SERVERS.NET | 3.4% |
| C.ROOT-SERVERS.NET | 21.1% |
| D.ROOT-SERVERS.NET | 2.6% |
| E.ROOT-SERVERS.NET | 12.3% |
| F.GTLD-SERVERS.NET | 4.0% |
| F.ROOT-SERVERS.NET | 12.3% |
| G.ROOT-SERVERS.NET | 62.1% |
| H.ROOT-SERVERS.NET | 20.9% |
| I.ROOT-SERVERS.NET | 7.1% |
| J.GTLD-SERVERS.NET | 8.3% |
| K.GTLD-SERVERS.NET | 2.2% |
| ns.eu.net | 30.0% |
| ns1.nic.uk | 8.0% |
| ns-nom.pipex.net | 2.5% |
| sec1.dns.uk.psi.net | 2.0% |

The top level domain servers are a key component of the Internet infrastructure, and should be designed to be very reliable. Yet, the experience show that many of them exhibit a loss rate much higher than the 5% value that we deduced from our analysis of connection delays. In fact, a few root servers like G, A, C, H exhibit particularly poor performance relative to other root servers; the same is true for the server managed by EUNET in London. The local DNS servers are supposed to constantly chase for the best servers, but it is not clear that they are doing a good job here.

The poor performance of some top level servers does not entirely explain the poor performance of the DNS. In particular, it does not explain the huge difference between the observed repetition rate for names in .EDU (10.6%) and .ORG (46.2%). There are two other possible explanations. First, the names in .EDU tend to be much more hierarchical than the name in .ORG. There are good chances that the name of major universities will be present in the caches of local servers, even if the name of small department servers are not. This means that the resolution of names in .EDU will rely much less on the performance of top level servers than the resolution of names in .GOV. Second, it is entirely possible that the servers in universities are connected at higher speed, for example through Internet2, and are generally more powerful and better managed than the servers of small non-profit organizations.

# Are we a special case?

All the measurement that we presented were taken from a work station connected to the local network of our laboratory. There is clearly a possibility that the results were influenced by the local conditions, such as the load of local DNS servers, or the capacity of the local Internet connections. To test whether our results were or were not representative, we got the help of several partners who accepted to run the same experiment from their own site. The results, for January 2000, are summarized in the following table:

| Host | Connect > 2sec | DNS > 2sec |
| --- | --- | --- |
| entropy.inria.fr | 9.7% | 24.4% |
| felix.argon.com | 1.7% | 27.8% |
| firedragon.eecs.umich.edu | 5.3% | 24.1% |
| elvis.Loudoun.mci.net | 3.7% | 26.4% |
| penguin.WPI.EDU | 3.2% | 29.0% |

The packet losses experience by the sites seem to vary a lot. For example, the INRIA site, located at Sophia Antipolis, in the south of France, is clearly experiencing higher packet losses than the other sites. This may be due either to the local conditions, or, more likely, to the high loss rate experienced in some international connections. On the other hand, all test sites report large values for the repeat rates of DNS transactions, values that are not out of line with our own experience.

# Conclusion

A major lesson of our study is that one always learns from measurements, specially for measurements that can be carried out over a long period of time. When we started daily measurements in September 1998, we expected to gain some insight on the evolution of basic parameters, such as the prevalent packet loss rate over the Internet. We obtained this result, and can say that, in general, from our point of view, the performance of the Internet has been improving. The average bandwidth available for a TCP connection increased, the media delays and the packet loss rates decreased. But the true value of measurement lies in the discovery of surprising results, and in the possibility of "mining the archive" to find explanation.

The most surprising result, in our case, is the poor performance of the domain name service. Name resolution, through the standard "gethostbyname()" interface, took longer than 2 seconds in 29% of our trials. We are not a special, aberrant case: control sites reported that in 24% to 32% of their trials, name resolution also took longer than 2 seconds. Albeit other factors may be at play, it appears that the main culprit is the flat structure of the domain name space, specially in the most popular domains, .com, .net and .org. This flat structure reduces the effectiveness of caching, and also concentrates the burden of solving names for the whole Internet on a very small set of servers. It is quite obvious that some of these servers cannot handle the load.

A clear limitation of our study is that measurements were conducted from a single point. We hope to enroll the cooperation of volunteers, to be able to probe a more significant part of the Internet.

We would like to seize the opportunity to acknowledge the contribution of Laura Cunningham, Walid Dabbous, Christophe Diot, Cheng Jin, Frank Kastenholtz, Beichuan Zhang and Lixia Zhang.

# References

- Sunil Kalidindi and Matthew J. Zekauskas, "Surveyor: An Infrastructure for Internet Performance Measurements," in Proc. of INET, (San Jose, California), Jun. 1999.

- Vern Paxson, "Measurements and Analysis of End-to-End Internet Dynamics," University of California at Berkeley, Berkeley, California, May 1997.

- Will E. Leland, Murad S. Taqq, Walter Willinger and Daniel V. Wilson, "On the self-similar nature of Ethernet traffic," in SIGCOMM Symposium on Communications Architectures and Protocols, Sidhu, Deepinder P., ed., (San Francisco, California), pp. 183--193, Sep. 1993.

- Michalis Faloutsos, Petros Faloutsos, Christos Faloutsos. On Power-Law Relationships of the Internet Topology, in ACM SIGCOMM'99 Conference, Computer Communication Review, Volume 29, Number 4, October 1999.

# Footnotes

This work was carried out and completed during the period that Christian Huitema was at Telcordia Technologies. His current affiliation is with Microsoft, and he can also be reached at huitema@microsoft.com.

This is self evident to the issue discussed above that results from our analysis applied only to overall performance while factors driving performance of individual network elements can dynamically change.